## Slide 1: Global dimensions to U.S. ozone pollution: Implications for air quality policy
Meiyun Lin
(Princeton University & NOAA GFDL)
Presentation to Environmental Defense Fund, April 25, 2017
Notes: 1

## Slide 2
Global dimensions to U.S. O3 air quality
Asia
Pacific
stratosphere
lightning
Wildfire, biogenic
North America
Rising Asian emissions
[e.g., Jacob et al., 1999;
Hilboll et al., 2013;
Lin et al., 2015b; 2017]
Natural events e.g., stratospheric [Langford et al, 2009; Lin et al., 2012; 2015a]; fires [Jaffe & Wigder, 2012]
Warming climate
+ in polluted regions
[Jacob & Winner, 2009 review]
+ natural sources
[Fiore et al., 2015 review; Lin et al., 2017]
? Transport pathways
[Lin et al., 2014]
X
CH4
“Background Ozone”
 Need process-level understanding on daily to MULTI-decadal time scaleS
2

## Slide 3
Fig. 17 from Lin et al. (ACP, 2017), data c/o R. Payton (EPA)
Challenges of a lowered U.S. O3 air quality standard
3
(ppb)
Mean Background in GFDL-AM3
(Lin et al., 2012ab; April-June 2010)
Los Angeles
Denver
70
Background
NAAQS
Obs. annual 4th highest MDA8 O3
2015 O3 NAAQS

## Slide 4
GFDL-AM3
Satellites
In situ
Surface networks
Late spring deep stratospheric intrusions over WUS and their links to climate variability
How does WUS surface O3 in spring and summer respond to rising Asian anthropogenic emissions and domestic NOx controls over the past two decades?
To what extent wildfire emissions contribute to WUS summertime O3 variability?
Eastern U.S. summertime O3 pollution: changing heat waves, droughts, and regional precursor emissions
Today’s presentation
4
Notes: Examples of how satellite, in situ measurements and models can be combined to detect and attribute non-controllable sources

## Slide 5: Deep stratospheric intrusions can push surface O3 to exceed the NAAQS level
GFDL-AM3
Lidar (Langford)
Flight track
30
60
150
90
120
[ppb]
Altitude (km)
S. California (May 23, 2010)
O3Strat
Background
(zero out US anthrop. emissions)
OBS, AM3
New standard
100
75
25
50
5
Surface O3 (ppb) , MDA8
May 24
Jun/1/2010
May/13/2010
CalNex2010
O3Strat
5
Lin M.Y. et al (JGR, 2012b), Springtime high surface ozone events over the WUS: Quantifying the role of stratospheric intrusions
Notes: Remember to introduce the O3Strat tracer
One day after, this intrusion pushed surface O3 to exceed 75 ppbv at Colorado Spring (2 km altitude)
BGO3: estimated by zeroing out N. American anthropogenic emissions in the model
Gray shading represents the range of ozone observations at sites within ~200 km diameter

## Slide 6
75th
25th
50th
6
Climate variability can modulate frequency of deep stratospheric intrusions
O3Strat
1990
Emissions held constant
Nudged to “real” winds
Stratospheric Contribution (ppb)
April-May
22 sites
(>1.5 km)
2012
Strong stratospheric influence on year-to-year variability on WUS surface ozone during spring
Lin M. et al. (Nature Communications, 2015)
Notes: Jet variability (internal or ENSO-forced)

## Slide 7
Developing ozone seasonal forecasts to aid western U.S. air quality planning
SST (C)
Regional preparations for an active stratospheric intrusion season
Deploy targeted measurements aimed at identifying “exceptional events”
Conduct daily forecast for public health alerts
Tropical SST cooling during La Niña peaks in winter
7
Lin M. et al (Nature Communications, 2015)
MDA8 O3 (ppb)
More frequent intrusions expected in the following spring over WUS?
Gothic Colorado Year 1999 (2.9 km asl)
O3Strat
BGO3
OBS
AM3
v
v
v

## Slide 8: Role of rising Asian anthropogenic emissions
Notes: AM3 O3Strat captures the episodic ozone enhancements although the mean baseline level of O3Strat may represent an upper limit

## Slide 9
Asian pollution contribution to WUS high-O3 events
Surface MDA8 O3
[ppb]
[ppb]
NAAQS
Lin M. et al [JGR, 2012a]: Transport of Asian O3 pollution into surface air over the WUS in spring
22-June-2010
Asian pollution can contribute ~20% on days when OBS > 60 ppb
OBS
Model
Asian
NASA AIRS CO
[1018 molecules cm-2]
9
Notes: Asian emissions contribute 8-12 ppb on days when OBS O3 ≥ 65 ppb (future NAAQS)
Consistent with elevated free trop O3 levels observed by in ozonesondes during CalNex

## Slide 10
RCP8.5 (AM3 BASE):
Almost tripled over 1980-2010
Largest increases in the 2000s
Peak in 2020-2030
50% reductions over 2000-2010 from the U.S. NOx SIP call
RCP4.5
Normalized to Y2000
RCP8.5
(AM3 BASE)
Satellites
Figure 1 of Lin et al. (ACP, 2017): Emission data from Lamarque et al. (2010, 2012);
Satellite (GOME/SCIAMACHY) NO2 data from KNMI (www.temis.nl)
Changes in anthropogenic emissions of NOx
10

## Slide 11: Model baseline sampling approach for evaluating O3 trends at WUS sites
Baseline
(Lassen)
Within a ~200x200 km2 model grid cell
Pollution
Observed spring MDA8 O3 trend 1988-2014
AM3_BASE surface
AM3_BASE 700 hPa, filtered
-0.8
-0.4
0.0
0.4
0.8
Lin, M., Horowitz L.W., Payton, R., Fiore, A.M., Tonnesen, T. [ACP, 2017]
Larger circles indicate significant trends (p<0.05)
ppb yr-1
11

## Slide 12
ppb yr-1
(MAM, 1988-2014)
Larger circles indicate significant trends (p<0.05)
OBS
AM3_BASE
50%
95%
5%
-0.8
-0.4
0.0
0.4
0.8
SPRING US surface MDA8 O3 trends over 1988-2014
Figure 7 from Lin et al. [ACP, 2017]
(Baseline filtering for WUS)
12

## Slide 13
SUMMER US surface MDA8 O3 trends over 1988-2014
ppb yr-1
-0.8
-0.4
0.0
0.4
0.8
Larger circles indicate significant trends (p<0.05)
Figure 8 from Lin M., et al. [ACP, 2017]
(Baseline filtering for WUS)
50%
95%
5%
OBS
AM3_BASE
13

## Slide 14: Median springtime MDA8 O3 trends at Great Basin NP
See Figure 13 of Lin et al. (ACP, 2017) for additional analysis for other sites
Most of the observed variability reflect changes in the background
The effects of US NOx controls (BASE minus NAB) are < 0.1 ppb yr-1
14

## Slide 15
Figure 10 from Lin et al. [ACP, 2017]
Background
ppb yr-1
Large circles indicate significant trends (p<0.05)
OBS
95th
50th
Observed vs modelled background O3 trends for SPRING
15

## Slide 16
Observed vs modelled background O3 trends for SUMMER
Figure 11 from Lin et al. [ACP, 2017]
OBS
ppb yr-1
Larger circles indicate significant trends (p<0.05)
Background
95th
50th
16
Notes: More emphasis on model evaluation of delta ozone changes

## Slide 17
2003-2012 minus 1981-1990
Asian (~50%)
CH4 (~15%)
Wildfires
(6% in spring; 12% in summer)
BASE
Meteorology
Background
Delta O3 [ppb]
MAM
JJA
Summarizing drivers of decadal mean O3 changes
from 1981-1990 to 2003-2012 over WUS
Figure 20 from Lin et al. [ACP, 2017]
17

## Slide 18: Summertime ozone variability and trends
Notes: AM3 O3Strat captures the episodic ozone enhancements although the mean baseline level of O3Strat may represent an upper limit

## Slide 19: Wildfires: NOT the primary driver of summer O3 IAV over WUS?
Figs 15 and 16 from Lin et al. [ACP, 2017]
Yellowstone NP (AUG)
High fire years
IAVFIRE – FIXEMIS (Aug2012)
6 ppb
-6
-0
Hot and dry summers:
deeper PBLH allowing more O3 to mix down to the surface (see also Zhang et al., 2014)
enhance regional O3 production and orographic lifting of urban pollution to mountaintop sites (e.g., Denver  Rocky Mountain NP)
Interannual correlations of YEL O3 w/ Tmax

## Slide 20
Observed declines in EUS summertime surface O3
following regional NOx reductions
Meiyun Lin et al. [ACP, 2017]
Pre-NOx SIP Call
(1988 Heat Wave)
Post-NOx SIP Call
(2012 Heat Wave)
Regional NOx reductions alleviated the O3 buildup during the recent 2012 heat wave relative to earlier heat waves (e.g., 1988)
20

## Slide 21
GFDL-AM3 captures interannual variability of O3 anomalies associated with high temperatures
Penn State University CASTNet site
O3 deposition sink to vegetation must be reduced by 35% in the model to match the observed anomaly during the severe drought of 1988
Meiyun Lin et al. [ACP, 2017]
R2 (OBS, AM3_BASE) = 0.67
R2 (OBS, AM3_FIXEMIS) = 0.30
July
1980
2015
DEP*0.65
21

## Slide 22
Influence of droughts on ozone removal
Meiyun Lin et al. [ACP, 2017]
Penn State Univ.
OBS
AM3 BASE
DEP*0.65
Reduced stomatal uptake under drought stress
Influence the highest ozone events above 100 ppb
Model challenges in simulating such land-biosphere couplings
22

## Slide 23
If NOx emissions had not declined, more frequent hot extremes since 1990 would have worsened the highest O3 events over EUS
Meiyun Lin et al. [ACP, 2017]
JJA
1990-2012 trend in biogenic isoprene emissions
95th percentile MDA8 O3 trend in AM3_FIXEMIS
1990-2012 trend in the frequency of warm days (above the 90th percentile for 1961-1990 base)
Larger circles indicate significant trends (p<0.05)
JJA
JJA

## Slide 24: Some final policy-relevant messages
The key driver of observed year-to-year variability in springtime high-O3 events >70 ppb at WUS rural sites
Need to develop forecast capabilities
drives much of multi-decadal WUS background O3 increases (50-65%; 0.2 ppb/yr), with lesser contribution from rising methane (~15%)
can enhance monthly mean MDA8 O3 at individual sites by 2-8 ppb in some summers
but not the primary driver of observed O3 year-to-year variability
Asian pollution
Late spring stratospheric intrusions
Wildfires
Lead to decreases in the highest pollution events in low-elevation US regions and during summer
guard against rising pollution levels triggered either by climate change or by global emission growth.
U.S. NOx emission controls
Need internationally collaborative efforts to mitigate global air pollution
Enormous progress made in the U.S. (e.g., Los Angeles) provides a template for Asian mega-cities (e.g. , Beijing)
Notes: Missing meteorology?

## Slide 25: Additional Slides for Q & A Discussions
Notes: AM3 O3Strat captures the episodic ozone enhancements although the mean baseline level of O3Strat may represent an upper limit

## Slide 26
For more information, please see the papers
Lin, M. et al (2012a): Transport of Asian ozone pollution into surface air over the western United States in spring (PDF)
Lin M. et al (2012b): Springtime high surface ozone events over the western United States: Quantifying the role of stratospheric intrusions (Full Text)
Lin, M. et al. (2014): Tropospheric ozone trends at Manna Loa Observatory tied to decadal climate variability (PDF)
Lin, M. et al. (2015a): Climate variability modulates western U.S. ozone air quality in spring via deep stratospheric intrusions (PDF)
Lin, M. et al. (2015b): Revisiting the evidence of increasing springtime ozone mixing ratios in the free troposphere over western North America, Geophysical Research Letter (PDF)
Lin, M. et al. (2017): U.S. surface ozone trends and extremes from 1980 to 2014: Quantifying the roles of rising Asian emissions, domestic controls, wildfires, and climate (PDF)
26

## Slide 27: Lin et al. (JGR2012a, 2012b)
Stratospheric and Asian influences
on springtime high-O3 events at WUS rural sites
Hi-Res GFDL-AM3
CASTNET (>1.5 km; Apr-Jun 2010)
Background
(Bias-corrected)
O3Strat
(Bias-corrected)
Asian
75th
25th
min
max
NAAQS
1:1 line
20
40
60
80
100
Notes: Up to here: 5-min

## Slide 28: Springtime ozone observed in Denver has increased at a rate similar to remote rural sites
Figure 17 from Lin et al. [ACP, 2017]

## Slide 29: Summertime O3 in Denver correlates with temperature
Fig. 17c from Lin et al. [ACP, 2017]
Role of VOCs from fires + urban NOx (Jaffe & Wigder,2012; Baker et al., 2016)?
Increased VOC emissions from oil and gas operations? But total VOC emissions may not be increasing over time due to the marked reductions in VOC emissions from vehicles [Bishop and Stedman, 2008, 2015]
Increased frequency of heat waves and air stagnation events (Horton et al., 2015)
Observed MDA8 O3
(Jul-Aug 95th )

## Slide 30
Projections of near-term changes in WUS lower trop. ozone in spring (March-April-May)
30
Normalized to 2000
Satellites
RCP8.5
RCP4.5
RCP8.5
RCP4.5
Global CH4 (ppb)
3000
2500
2000
1500
E. China NOx emissions
1980
30
OBS (GRB, LAV, ROM)
AM3 BASE, nudged
Figure 14 from Lin et al. [ACP, 2017]

## Slide 31
Baseline O3 trends derived from observations and free-running chemistry-climate models differ by a factor of 2 (Parrish et al., 2014)
OBS (Spring)
Free-running CMIP5 models
These discrepancies reflect a combination of factors:
(1) Internal climate variability (Lin et al., 2014; 2015a; Barnes et al., 2016)
(2) Measurement sampling biases (Lin et al., 2015b)
(3) Model difficulty resolving observed remote baseline conditions (Lin et al., 2017)
Mt. Happo
Japanese MBL
U.S. Pacific MBL
N. American FT
Lassen NP
Need model hindcasts driven by observed meteorology (next slide)
Notes: Remember to define baseline
Concerns …

## Slide 32: Influence of measurement sampling biases
Lin, M.; Horowitz, LW; Cooper, OR et al. [GRL, 2015]
Ozone Anomaly (ppb)
Year (April-May)
[Cooper et al.]
[Cooper2010, Nature]
Year (April-May)
32
Western N. American FT (3-8 km altitude)
15-year trends driven by internal climate variability can be as large as emission-driven trends.
Even with co-sampling, free-running CCMs are not expected to reproduce the trends.
Nudged to “real” winds
BASE true average
Sampling biases
40
60
80
1984
2005
FIXEMIS 500hPa O3
Notes: 26 min up to here

## Slide 33
Probability Density
33
Neutral: µ = 56.5,σ = 7.5
El Niño (1998, 2010): µ = 56.9,σ = 7.3
La Niña (1999, 2008, 2011): µ = 58.5,σ = 7.9
Pinatubo (1992, 1993): µ = 54.3,σ = 6.5
Observed daily max 8-h average O3 [ppbv], Apr-May
Statistical testing
Observed changes in surface O3 distribution,
particularly in the upper tail
Lin M. et al (Nature Communications, 2015)
Little change in WUS surface air during El Niño despite increased UTLS O3 burdens reported previously [e.g. Langford1998; Bronnimann2004; Neu2014].
Notes: Tied to Neu paper …

## Slide 34
Surface O3 distribution in high vs low background springs
1991
1999
2008
2011
2012
1992
1993
Meiyun Lin et al. (Nature Communications, 2015)
(N. American anthrop. emissions set to zero)
Probability Density
34
NAAQS
Notes: As our national ozone standard becomes more stringent, the relative importance of these stratospheric intrusions grows, leaving less room for U.S. anthropogenic emissions to contribute to ozone pollution prior to exceeding the level set by the U.S. EPA.